## Slide 1
Emergency messages when the network fails
EMERGENCYMESH / 01
Disasters can interrupt mobile networks and internet.
Nearby Android phones carry messages and SOS alerts until a path to the recipient appears.
Slackers • CBIT Hacktoberfest 2026
Notes: Problem and project scope. A prototype, not an emergency service.

## Slide 2
A message can travel through another phone
EMERGENCYMESH / 02
A (vivo) sent through B (Samsung) to C (OnePlus).
C delivered in 2.6 seconds, one hop. Pending survived restart and sent after reconnection.
SOS arrived before 20 queued ordinary messages.
Core run: all three phones offline.
Notes: Sources: docs/evidence/final-build.md and docs/evidence/required-features.md. A-C radio blocked by allowlist; all three phones airplane mode on, Bluetooth on, Wi-Fi off.

## Slide 3
Android mesh and response tools
EMERGENCYMESH / 03
Compose interface and Room message queue
Nearby Connections relay and delivery acknowledgements
Tink protection and Android Keystore identity
Tested extras: Call-Out, Talk-Back, Last Breath, Bluetooth-name SOS, laptop relay and dashboard
Notes: Architecture: app Compose/Kotlin, Room, Nearby Connections, Tink and Android Keystore. Extras source docs/evidence/extras-phone-test.md; laptop and dashboard through USB adb reverse, not phone-to-laptop Wi-Fi. AI was off.

## Slide 4
Evidence from three Android brands
EMERGENCYMESH / 04
vivo V2404
Samsung SM-S721B
OnePlus CPH2569
Offline relay: 2.6 s. Four-stage status timeline.
Locked Samsung passed; vivo needed settings; OnePlus froze.
Notes: Sources: docs/evidence/final-build.md, required-features.md, extras-phone-test.md. Three phones, 119/119 tests for the final core build. Do not claim all extras were fully offline.

## Slide 5
What the tests did not establish
EMERGENCYMESH / 05
Locked relay varied by phone brand; OnePlus froze despite exemptions.
Extras run: A had internet, all phones were on USB power.
Laptop and dashboard tests used a USB bridge; AI model was off.
Range, battery drain and real no-app phone remain untested.
Notes: Source: docs/evidence/extras-phone-test.md and final-build.md. Battery and range may be updated if later evidence is measured. Laptop and dashboard were over USB adb reverse. A had internet in extras run. No real AI key.

## Slide 6
What the mentors asked and what we changed
EMERGENCYMESH / 06
Relay, acknowledgement and queued recovery passed on three phones.
A new status timeline keeps Relayed visible after delivery.
Shortest-path routing and responder/admin changes:
Pending final merge and phone recheck.
Notes: Routing and User/Responder/Admin area roles are being built on separate branches. Verify merged final APK on phones before presenting them as completed. Status timeline was tested in final-build.md.